## Slide 1: Advanced LabViEW
http://workshop.frclabviewtutorials.com

## Slide 2: Customizing the Dashboard

## Slide 3: Customizing the Dashboard
Open Project
Notes: demo

## Slide 4: Customizing the Dashboard
Open Project
Sending data from robot

## Slide 5: Customizing the Dashboard
Open Project
Sending data from robot
  Smart Dashboard VI’s
  Named (case sensitive) values

## Slide 6: Sensors

## Slide 7: Sensors - Encoder

## Slide 8: Sensors - Encoder
Places to use encoders:
  When trying to measure rotational speed
  Trying to measure rotational distances possibly greater than 8 rotations.
  Don’t care about starting position

## Slide 9: Sensors - Encoder
Places to use encoders:
  When trying to measure rotation speed
  Trying to measure rotational distances possibly greater than 8 rotations.
  Don’t care about starting position
Examples:
  Drive train
  Fly Wheel/wheeled shooter
Notes: Drive-train
likely to travel more than 10 rotations in a given match
Don’t care where the wheels are when starting, and even better – the robots starting position is 0 (good)
Fly Wheel
Don’t care what position it starts in
Likely to rotate more than 10 rotations in a match
Care is primarily about speed

## Slide 10: Sensors - Encoder
Reading

## Slide 11: Sensors - Encoder
Control

## Slide 12: Sensors - Potentiometer
Notes: TODO: Code

## Slide 13: Sensors - Potentiometer
Places to use potentiometers:
  Trying to measure rotational distances less than 8 rotations.
  Care about starting position – or absolute positions
Examples:
  Arm angles
  Elevator positions
Notes: Arm angles:
Care about absolute position (0 should always mean on the ground regardless of where the arm was when we turn it on).
Same for elevators and similar manipulators

## Slide 14: Sensors - Potentiometer
Control

## Slide 15: Sensors - Potentiometer
Note:
  Easy way to make potentiometer relative to a known point:
https://www.frclabviewtutorials.com/tutorials/sensors/roborio/potentiometer/
Notes: One disadvantage that potentiometers have when compared to encoders is now you care very much about the position of the potentiometer when mounting/unmounting it.
I’m not going to go into this today, but there is a documented, simple way to apply a known offset when reading potentiometers – you would then update this offset after doing modifications.

## Slide 16: Sensors - Gyro

## Slide 17: Sensors - Gyro
Places to use a Gyro:
  When trying to drive perfectly straight
  When trying to turn to specific angles (especially in auto)

## Slide 18: Sensors - Gyro
Control

## Slide 19: PID
Proportional
Notes: https://docs.google.com/viewer?a=v&pid=sites&srcid=aGFyZGluZy5lZHV8dGVhbS0zOTM3fGd4OjUyNzdiNzRkNjkxNjA3MGM
https://www.youtube.com/watch?v=JEpWlTl95Tw
https://www.youtube.com/watch?v=UR0hOmjaHp0
http://robotics.stackexchange.com/questions/167/what-are-good-strategies-for-tuning-pid-loops

## Slide 20: PID
Proportional
  Constant multiplied by error (offset)
  The larger this is, the faster the robot approaches the setpoint (smaller rise time)

## Slide 21: PID
Proportional
  Constant multiplied by error (offset)
  The larger this is, the faster the robot approaches the setpoint (smaller rise time)
Integral
  Constant multiplied by integral of all previous error values
  The larger this is, the less overshoot and settling time (less bounce)

## Slide 22: PID
Proportional
  Constant multiplied by error (offset)
  The larger this is, the faster the robot approaches the setpoint (smaller rise time)
Integral
  Constant multiplied by integral of all previous error values
  The larger this is, the less overshoot and settling time (less bounce)
Differential
  Used to eliminate steady state error (reducing offset after movement)

## Slide 23: PID
Proportional
  Constant multiplied by error (offset)
  The larger this is, the faster the robot approaches the setpoint (smaller rise time)
Integral
  Constant multiplied by integral of all previous error values
  The larger this is, the less overshoot and settling time (less bounce)
Differential
  Used to eliminate steady state error (reducing offset after movement)

## Slide 24: PID
Tuning

## Slide 25: PID
Tuning
  Several methods available
    Ziegler–Nichols*
    Tyreus Luyben
    Cohen–Coon
    Åström-Hägglund
    Manual Tuning*
Notes: http://faculty.mercer.edu/jenkins_he/documents/TuningforPIDControllers.pdf#page=6
https://www.youtube.com/watch?v=JEpWlTl95Tw
https://www.youtube.com/watch?v=UR0hOmjaHp0
http://robotics.stackexchange.com/questions/167/what-are-good-strategies-for-tuning-pid-loops
Ziegler-Nichols: http://robotsforroboticists.com/pid-control/
Manual (page 16): https://docs.google.com/viewer?a=v&pid=sites&srcid=aGFyZGluZy5lZHV8dGVhbS0zOTM3fGd4OjUyNzdiNzRkNjkxNjA3MGM
http://www.ni.com/white-paper/3782/en/

## Slide 26: PID
Tuning
  Manuel
    Raise CP Until robot oscillates about setpoint
    Raise CD Until Robot stops bouncing
    Raise CI (and change the setpoint) until robot turns and hits the target point
  Ziegler-Nichols
    Raise CP Until robot oscillates (Value of CP becomes Ku)
    Measure the period of this oscillation (Time to complete 1 cycle becomes TU)

## Slide 27: PID
Tuning
  Manuel
    Raise CP Until robot oscillates about setpoint
    Raise CD Until Robot stops bouncing
    Raise CI (and change the setpoint) until robot turns and hits the target point
  Ziegler-Nichols
    Raise CP Until robot oscillates (Value of CP becomes Ku)
    Measure the period of this oscillation (Time to complete 1 cycle becomes TU)

## Slide 28: PID
Tuning
  Manuel
    Raise CP Until robot oscillates about setpoint
    Raise CD Until Robot stops bouncing
    Raise CI (and change the setpoint) until robot turns and hits the target point
  Ziegler-Nichols
    Raise CP Until robot oscillates (Value of CP becomes Ku)
    Measure the period of this oscillation (Time to complete 1 cycle becomes TU)

## Slide 29: PID
Demo

## Slide 30: Architectures
State Machine

## Slide 31: Architectures
State Machine

## Slide 32: Architectures
State Machine

## Slide 33: Architectures
State Machine
Producer-Consumer
  Parallel loops
    First creating data or instructions
    Other handling

## Slide 34: Architectures
State Machine
Producer-Consumer
  Parallel loops
  Use either queue or fgv

## Slide 35: Producer Consumer Demo
Notes: Queue and FGV

## Slide 36: Type Def.
Useful for passing data – both controls and indicators
Demo

## Slide 37: Type Def.
Useful for passing data – both controls and indicators
Demo
Notes: typedefs

## Slide 38: Questions